## Slide 1: Omnimagnet Mind Map
Mohamed Ghori:
www.linkedin.com/in/mohamedghori , https://github.com/mghorireserach
Aaron Becker:
http://www.ece.uh.edu/faculty/becker
Inspired by Dr. Jake Abbott:
http://www.telerobotics.utah.edu/index.php/Research/Omnimagnets

## Slide 2: Mind Map
MAIN
SHAPE
CNTRL
MATH
Data
VISUAL
MAIN
Master Function to run entire Omnimagnet Simulation.
SHAPE
Trajectory Shape Function that rolls the ball through a specific trajectory. Using CNTRL it returns a VISUAL & DATA
CNTRL
Trajectory Following Function that uses MATH to output DATA & Visual
MATH
Math Tools (ie. rotx.m : rotation about the x-axis )
VISUAL
Visualization of the tool’s simulated trajectory
DATA
Solenoid Current Values

## Slide 3: MAIN
MAIN( type, x0, y0, phi, psi, ShapeSize, T, dt, speed, ballsize )
The MAIN function is the highest level function where the rollBallInSquare function and the playback function is called, as well as functions that clear all the figures & clear all the data. The main function has 10 parameters. However, it can be called with 1,6,9, or 10 arguments.
MAP
SHAPE

## Slide 4: SHAPE
MAP
CNTRL
rollBallInSquare ( x0, y0, phi, psi, ShapeSize, T, dt, speed, ballsize )
rollBallInCirlce ( x0, y0, phi, psi, ShapeSize, T, dt, speed, ballsize)
Playback (currx, curry, currz,wHb)

## Slide 5: rollBallInSquare
Note:
Rectangle parallel to x-y axies
Speed of Ball
Perimeter period = velocity desired
Period for a leg = Leg length velocity desired
Moving Point to point
ballfwd called to connect between corners
ballfwd outputs solenoid current values along each path
Output
Solenoid-currents concatenated and output (OLD)
Output an array of North Pole Vectors
Magnet
N
Velocity
SHAPE

## Slide 6: rollBallInCircle
Note:
Circle about center (0,0)
Speed of Ball
Perimeter period = velocity desired
Period for a leg = Leg length velocity desired
Moving Point to point
ballfwd called to connect between corners
ballfwd outputs solenoid current values along each path
Output
Solenoid-currents concatenated and output
Magnet
N
Velocity
SHAPE

## Slide 7: playback
Moving Point from Orientation to Orientation
The North-Pole vectors that were recorded are used with fwdcurrent to rotate between such that the north pole coincides with the final north pole vector.
Output
A visual of the ball tool following this path
SHAPE
Magnet
N
Velocity

## Slide 8: CNTRL
MAP
MATH
Ballfwd ( p0, pf, wHb, T, dt, speed, ballsize )
Fwdcurrent ( I0, If, wHb, T, dt, speed, ballsize )
fwdMagneticField ( currx, curry, currz, x, y )
inverseMagneticField ( x, y, phi, psi )

## Slide 9: ballfwd
Note:
Rolling about Magnetic Field y-Axis
Method
Find Goal:
Rotate about world z-axis
T(ballfwd Period)/4
Return current for orientation snapshots at “0 : dt :T/4”
Roll to Goal:
Rotate about Magnetic Field y-Axis
3T/4
Return current for orientation snapshots at “T/4 : dt : T”
Output
currx, curry , currz vectors for solenoid-current input
CNTRL

## Slide 10: fwdcurrent
Note:
Rotates magnetic Field around single axis
Rotating Tool
Method:
Two consecutive orientations are found using two consecutive current vectors
The orientations are decomposed in terms of rotation in the xy-plane(phi) & the xz-plane(psi)
The difference in psi and phi are then converted to a rotation matrix
This rotation matrix is decomposed into an axis and angle rotation
The magnetic field is then rotated about this axis
The linear velocity consists of the rotation vector in the xy-plane
Output:
Final Position and Orientation (pf, wRb)
CNTRL

## Slide 11: fwdMagneticField
Note:
The equations are not linear and there fore when back tracking one does not find the same vectors
Input:
Electric Current for each solenoid (currx,curry,currz)
Current Position of Ball (x,y)
EQN:
Current put in as a vector into equation from Jake Abbott
Output:
Magnetic Field Vector Tangent to Magnetic Field at the Tool
CNTRL

## Slide 12: inverseMagneticField
Input:
Orientation of the magnetic field at the Tool (phi,psi)
Current Position of Ball (x,y)
EQN:
Magnetic Field vector constructed using orientation with a magnitude of 100
Magnetic Field vector put into equation from Jake Abbott
Output:
Electric Current for each solenoid [currx; curry; currz]
CNTRL

## Slide 13: MATH
piont2piontroll (vect1,vect2)
rotTime (deltheta,omega0, alph)
Rot_in_phipsi (R)
Vect2skew (vector)
Axis2rot (Axis,Angle)
rot2Axis (R)
rot2quat(R)
quatmult (q1,q2)
Rotx (roll)
Roty (pitch)
Rotz (yaw)
MAP
VISUAL

## Slide 14: point2piontroll
Implemented Dr. Becker's Code: "Roll Any Point on the Sphere to any desired Latitude-Longitude Coordinates with one Straight-Line Roll“
MATH

## Slide 15: rotTime
Uses kinematic th = th0 + w0*t + 0.5*alph*t^2 to calculate the time required to reach a certain position using a given angular acceleration(from torque)
MATH

## Slide 16: Rot_in_phipsi
This function returns the phi (angle of vector with the x-axis in x-z plane) and psi (angle of vector the x-axis in the y-x-plane )
MATH

## Slide 17: findPhiPsi
Using “arccos” to find the angle from the world x-axis in the zx-plane (psi)
Using “arccos” to find the angle from the world x-axis in the xy-plane (phi)
MATH

## Slide 18: anglediff
Find the angle of the two vectors with respect to the world x-axis in the xy-plane
The difference between these two angles is the angle between vectors
MATH

## Slide 19: vect2skew
Converts from a vector its skew symmetric matrix form
MATH
Unit-Vector
Skew-Symmetric Form

## Slide 20: axis2rot
Converts from an axis angle notation of a rotation to a rotation matrix in 3D Euclidean space
MATH

## Slide 21: rot2axis
Converts from a rotation matrix to an axis angle notation for rotation in 3D euclidean space
MATH

## Slide 22: rot2quat
Converts a rotation matrix into its quaternion form

## Slide 23: quatmult
A function that multiplies two quaternions

## Slide 24: rotx roty rotz
Basic Euler rotation matrix equations (roll, pitch, yaw)
MATH

## Slide 25: VISUAL
plot_ball (ballsize, pos,R,dt,speed)
Showmagfield (currx,curry,currz,p0)
Magfield (I)
MAP
DATA

## Slide 26: plot_ball
First Call creates a figure of equal axis at a corner view
Draws a transparent sphere
Draws a quiver along the z-axis and y-axis of the magnetic field
Then transforms it using a homogeneous matrix (MATLAB:hgtransform)
VISUAL

## Slide 27: showmagfield
Draws a magnetic field line using a series of 200 segments (quivers) from head to tail

## Slide 28: magfield
Draws the magnetic field based on the solenoid current
NOTE: Does not use meshgrid
NOTE: The entire field is pointing in one direction (which may be incorrect)

## Slide 29: DATA
Solenoid-current(curra, currb, currc)
MAP