## Slide 1: Omnimagnet Mind Map
Mohamed Ghori

## Slide 2: Mind Map
MAIN
SHAPE
CNTRL
MATH
Data
VISUAL
MAIN
Master Function to run entire Omnimagnet Simulation.
SHAPE
Trajectory Shape Function that rolls the ball through a specific trajectory. Using CNTRL it returns a VISUAL & DATA
CNTRL
Trajectory Following Function that uses MATH to output DATA & Visual
MATH
Math Tools (ie. rotx.m : rotation about the x-axis )
VISUAL
Visualization of the tool’s simulated trajectory
DATA
Solenoid Current Values

## Slide 3: MAIN
TYPE
INITIAL POSITION & ORIENTATION & SHAPEVALUE
PERIOD & TIME STEP
VIDEO SPEED & TOOL SIZE
MAP
MAIN( type, x0, y0, phi, psi, ShapeSize, T, dt, speed, ballsize )
SHAPE

## Slide 4: TYPE
1: Square/Rectangular Shape
2: Circle
TYPE
MAIN

## Slide 5: INITIAL POSITION & ORIENTATION & SHAPEVALUE
Initial Position
X0 : initial x position
Y0: initial y position
Initial Orientation
Phi: longitudinal position of north pole
Psi: latitudinal position of north pole
Defining value of trajectory’s shape
Shapevalue: defining value for shape
  (rectangle = [corner-x, conrer-y])
  (Circle = radius)
INITIAL POSITION & ORIENTATION & SHAPEVALUE
MAIN
SHAPE

## Slide 6: PERIOD & TIME STEP
T : time to complete task
dt: time steps to record/observe
PERIOD & TIME STEP
MAIN
SHAPE

## Slide 7: VIDEO SPEED & TOOL SIZE
Speed: multiplier that speeds up the visualization
Tool Size: defines the size(radius) of the magnetic tool
VIDEO SPEED & TOOL SIZE
MAIN
SHAPE

## Slide 8: SHAPE
rollBallInSquare( x0, y0, phi, psi, ShapeSize, T, dt, speed, ballsize )
rollBallInCirlce( x0, y0, phi, psi, ShapeSize, T, dt, speed, ballsize )
INITIAL POSITION & ORIENTATION & SHAPEVALUE
PERIOD & TIME STEP
VIDEO SPEED & TOOL SIZE
MAP
CNTRL

## Slide 9: rollBallInSquare
Note:
Rectangle parallel to x-y axies
Speed of Ball
Perimeter period = velocity desired
Period for a leg = Leg length velocity desired
Moving Point to point
ballfwd called to connect between corners
ballfwd outputs solenoid current values along each path
Output
Solenoid-currents concatenated and output
Magnet
N
Velocity
SHAPE

## Slide 10: rollBallInCircle
Note:
Circle about center (0,0)
Speed of Ball
Perimeter period = velocity desired
Period for a leg = Leg length velocity desired
Moving Point to point
ballfwd called to connect between corners
ballfwd outputs solenoid current values along each path
Output
Solenoid-currents concatenated and output
Magnet
N
Velocity
SHAPE

## Slide 11: CNTRL
Ballfwd (p0, pf, wRb, T, dt, speed, ballsize )
Fwdcurrent (I0, If, wRb, T, dt, speed, ballsize )
fwdMagneticField (currx, curry, currz, x, y )
inverseMagneticField (x, y, phi, psi)
MAP
MATH

## Slide 12: ballfwd
Note:
Rolling about Magnetic Field y-Axis
Find Goal:
Rotate about world z-axis
T(ballfwd Period)/4
Return current for orientation snapshots at “0 : dt :T/4”
Roll to Goal:
Rotate about Magnetic Field y-Axis
3T/4
Return current for orientation snapshots at “T/4 : dt : T”
CNTRL

## Slide 13: fwdcurrent
Note:
Rotates magnetic Field around single axis
Rotating Tool
Method:
Two consecutive orientations are found using two consecutive current vectors
The orientations are decomposed in terms of rotation in the xy-plane(phi) & the xz-plane(psi)
The difference in psi and phi are then converted to a rotation matrix
This rotation matrix is decomposed into an axis and angle rotation
The magnetic field is then rotated about this axis
The linear velocity consists of the rotation vector in the xy-plane
Output:
Final Position and Orientation (pf, wRb)
CNTRL

## Slide 14: fwdMagneticField
Input:
Electric Current for each solenoid (currx,curry,currz)
Current Position of Ball (x,y)
EQN:
Current put in as a vector into equation from Jake Abbott
Output:
Magnetic Field Vector Tangent to Magnetic Field at the Tool
CNTRL

## Slide 15: inverseMagneticField
Input:
Orientation of the magnetic field at the Tool (phi,psi)
Current Position of Ball (x,y)
EQN:
Magnetic Field vector constructed using orientation with a magnitude of 100
Magnetic Field vector put into equation from Jake Abbott
Output:
Electric Current for each solenoid [currx; curry; currz]
CNTRL

## Slide 16: MATH
anglediff (vect1,vect2);
findPhiPsi (R)
Vect2skew (vector)
Rotx (roll)
Roty (pitch)
Rotz (yaw)
HomoMatrix (rpy, pos)
MAP
VISUAL

## Slide 17: anglediff
Find the angle of the two vectors with respect to the world x-axis in the xy-plane
The difference between these two angles is the angle between vectors
MATH

## Slide 18: findPhiPsi
Using “arccos” to find the angle from the world x-axis in the zx-plane (psi)
Using “arccos” to find the angle from the world x-axis in the xy-plane (phi)
MATH

## Slide 19: vect2skew
Converts from a vector its skew symmetric matrix form
MATH

## Slide 20: rotx roty rotz
Basic Euler rotation matrix equations (roll, pitch, yaw)
MATH

## Slide 21: HomoMatrix
Creates a homogeneous matrix from a position and a vector of [roll pitch yaw]
MATH

## Slide 22: VISUAL
plot_ball(ballsize,pos,R,dt,speed)
Showmagfield(currx,curry,currz,p0)
MAP
DATA

## Slide 23: plot_ball
First Call creates a figure of equal axis at a corner view
Draws a transparent sphere
Draws a quiver along the z-axis and y-axis of the magnetic field
VISUAL

## Slide 24: showmagfield
Draws a magnetic field line using a series of 200 segments (quivers) from head to tail

## Slide 25: DATA
Solenoid-current(curra, currb, currc)
MAP